## Slide 1: FAST TRACK TO SUCCESS
SLAB TRACK SOLUTION OF STABIRAIL COMBINES ACCURACY AND DURABILITY

## Slide 2: Equipment
Complete Stabirail equipment:
Concrete Milling Machine
Diamond Drilling train
Anchoring Train
Tanker (10 000 litres water and 2 500 litres diesel)
Lorry with water tank

## Slide 3: Working method
Concrete Milling Machine:
mills the concrete rail beds with millimeter accuracy

## Slide 4: Working method
Concrete Milling Machine:
rail beds are milled simultaneously

## Slide 5: Working method
Concrete Milling Machine:
operated by 3D system

## Slide 6: Working method
Concrete Milling Machine:
capable of working on parabolic transitional curves and transitional slopes

## Slide 7: Working method
Concrete Milling Machine:
diamond discs are water cooled (no dust formation)

## Slide 8: Working method
Concrete Milling Machine:
sludge is separated

## Slide 9: Working method
Concrete Milling Machine:
cooling water is reused

## Slide 10: Working method
Concrete Milling Machine:
operates autonomously

## Slide 11: Working method
Drilling Train:
Cores diamond drilled holes in the concrete bed

## Slide 12: Working method
Drilling Train:
Water cooled
Works autonomously

## Slide 13: Working method
Anchoring Train:
Cleans the holes

## Slide 14: Working method
Anchoring Train:
Fixes the anchors with a chemical adhisive
Works autonomously

## Slide 15: Efficiency
Concrete Milling Machine
At max. 10 mm to be milled
At max. 20 mm to be milled
* Limestone based concrete
200 m/8h – 600 m/24h
135 m/8 h – 400 m/24h

## Slide 16: Efficiency
Drilling Train:
150m/8h = 450m/24h*
  Limestone based concrete
  Max. coring diameter: 32mm
  Max. coring dept: 130mm
  Max. diameter of rebar: 12mm

## Slide 17: Efficiency
Anchoring Train:
Cleaning drilled holes
Achoring drilled holes
300 m/8h – 900 m/24h
300 m/8 h – 900 m/24h
1 machine, 2 actions
=
150m/8h

## Slide 18: Advantages
Advantages:
Fast working method (200m/8h)
No movement of the machines IN and OUT of the tunnel; the machines remain on site
2 mm accuracy
Reduced vibration to the tunnel construction and buildings above
Shallow construction height of the tunnel
Reduced dead load
Higher speed operation
Very low maintenance requirements
Long design life = Low whole-life cost

## Slide 19: Drawings
Drawings:

## Slide 20: Drawings
Drawings:

## Slide 21: Drawings
Drawings:

## Slide 22: Drawings
Drawings:

## Slide 23: Drawings
Drawings:

## Slide 24: Drawings
Drawings:

## Slide 25: Drawings
Drawings:

## Slide 26: Drawings
Drawings:

## Slide 27: References
Antwerp Central Station
8,3 km track length 53 484 rail anchors
5 rail switches 2 463 rail anchors
2004

## Slide 28: References
Diabolo Tunnel
9,5 km track length 60 620 rail anchors
10 rail switches 7 480 rail anchors
Brussels Airport 2009

## Slide 29: References
Liefkenshoektunnel
16,6 km track length 110 564 rail anchors
Port of Antwerp 2013

## Slide 30: References
Shuman JosaphatTunnel
4,2 km track length 27 168 rail anchors
5 rail switches 2 357 rail anchors
Brussels 2014

## Slide 31: FAST TRACK TO SUCCESS
Contact us for a visit or more information
Watch our video on www.stabirail.com